+5V
GND
Relay Inputs

LED 24V in

Hand Held Controller power
TLL to Arduino
Control LEDs out
RS422 to Hand Held Controller
Inverter Control Pins
Sensor Connector
Digital Sinking Outputs
General Cable Colour Rules
Brown = input
Blue = serial send/output
Green = serial receive/sensor read
White = digital signal
Red = +5V
Black = GND
Horrible light pink = 24V

Pin assignments
Digital Sinking Outputs
The output pins are assigned to:
"R-RGC","R-RGD","R-GER1","R-GER2","R-GES","R-LTF","R-LTR","Z-BR-PLC","R-WHS","R-CSRT","R-FSH","R-CSSB","R-MIE","R-CEN","STF","STR","RM1","RH1","RM2","RH2","LEDG","LEDR"
Where “R-RGC” is pin 22 and each item in the above list increments the pin number by one.

Pin 1

MOLEX 1 – relay drive					MOLEX 2 – relay drive
RGC	RGD	GER1	GER2	GES	LTF	LTR	GND	Z-BR	WHS	CSRT	FSH	CSSB	MIE	CEN	GND

Inverter Control Pins

Pin 1
INVERTER DRIVE
Forward	Reverse	INV1M	INV1H	INV2M	INV2H	+24V	NC/GND

Relay Inputs

Pin 1
RELAY READ INPUT
R-IN1	R-IN2	R-IN3	R-IN4	R-IN5	R-IN6	Inverter Health	COMMON

Sensor Connector

Pin 1
Difficult to see I know but this is the bottom right angle Molex connector viewed from above.
SENSORS INPUT
SPD1	SPD2	+5V	GND	24VBRC*	NC	THM1	GND	THM2	GND

*BRC = Brake Resistor Contactor
LED 24V In

Pin 1
LED 24V
+24V in	NC	NC	NC

Control LED Out

LED Out
LED1 (24V)	LED2 (24V)	GND	GND

ARDUINO:
The Arduino is now powered by the 24-5V DC-DC converter. It is still perfectly fine to plug a USB cable in as well, the ARDUINO automatically uses the power from the DC-DC converter and not the USB port. This enables easy debugging.
SOFTWARE:
The available commands are (all lower case):
- list – displays all output pins, their name and state.
- speed1 – puts both inverters to speed1
- speed2 – as above
- speed3 – as above
- speed4 - as above
- forward – set inverters forward
- backward – set inverters backward
- coast – set inverters coast
- startgen – attempt to start generator
- stopgen – stop generator
- sensors – print thermistor and speed sense readings.
- flick – flip the state of every output pin twice in pin number order.
- Any Number – e.g. 22 flip state of pin 22.